## Slide 1: Micro Cognitive Radio Network Testbed (MICRONET) for education, experimentation, and demonstration
Eric Sollenberger
Vuk Marojevic
Carl Dietrich
Sponsored by wireless@vt
Virginia Tech

## Slide 2: Outline
Motivation
Implementation
Initial experimentation
Limitations
Additional plans
Conclusion

## Slide 3: Micronet: Motivation
Testbed Design Goals
Inexpensive
User friendly
Portable
Multiple node support
CORNET
Price ($)
Radio Nodes
Size
Bandwidth (MHz)
Maximum Frequency (GHz)
<$100
$100-$1k
$1k-$10k
>$100k
1
<5
5-25
25-50
50-100
<1
1-5
5-20
20-60
>60
<1
1-2.5
2.5-6
6-30
>30
Handheld
Desk
Room
Building
City
$10k-$100k
Micronet

## Slide 4: Micronet: Hardware
Item | Qty | Supplier
Dell Latitude 2100 | 1 | Ebay (used)
Raspberry Pi | 1 | Newark
RTL2832 R820T | 3 | Ebay
RTL2832 E4000 | 1 | Ebay
8 Gb SD Card | 1 | Best Buy
10’ USB Extension | 3 | Sweetwater
Micro USB power cable | 1 | MCM Electronics
Ethernet cable | 2 | Rakuten.com
TP-Link Ethernet Switch | 1 | Newegg
Block Diagram
Photo
Bill of Materials

## Slide 5: Micronet: The Raspberry Pi as a Transmitter
PiFM
C++ code
Tx frequency range: 1 - 250 MHz
Approximate Tx distance: 100 m
Reads .wav files
Added functionality
FSK/OOK modulation

## Slide 6: Micronet: Software
GNU Radio Companion: FM Receiver Flowgraph
Installed Packages:
GNU Radio
liquid-dsp
Pyrtlsdr
RTLSDR Scanner
kalibrate-rtl
XRDP
GNU Radio : FFT plot

## Slide 7: Micronet: Sample Experiments
FM demodulation/mixer
Raw sample file writes
Spectrum sensing
Antenna diversity
FSK/OOK
Basic DSA

## Slide 8: Micronet: FM Mixer

## Slide 9: Micronet: FM Mixer

## Slide 10: Micronet: Spectrum Sensing
RTLSDR Scanner
RTLSDR Spectrum Sense

## Slide 11: Micronet: Antenna Selection Diversity

## Slide 12: Micronet: FSK Tx/Rx

## Slide 13: Micronet: Basic DSA
Procedure
Scan allowable transmit frequency range
Determine optimal transmit channel based on channel power and adjacent channel powers
Transmit a single burst
Recheck vacancy of channel

## Slide 14: Micronet: Additional Plans
Experiments
SDR position estimation
Antenna diversity
Phased antenna arrays
Basic DSA algorithms
CR coexistence with CORNET
Development
Raspberry Pi Transmission
  Integration with SDR tools
  Optimization/Measurement of performance (BER)
  Demo’s/applications
  Hardware augmentation

## Slide 15: Conclusion
What has been achieved/demonstrated
Creation of a CR testbed that is:
  Low cost
  Flexible/portable
  Supports multiple radio nodes
  Has the potential for many diverse experiments
Identified limitations
  Processing power
  Bandwidth
  Tx capabilities
    Limited modulation schemes
    Lack of power control
    Spurious signal